## Slide 1
Mass Wasting:

## Slide 2
Landslides or slope movements can be classified in many ways…
There are many attributes used as criteria for identification and classification including:
#1 - Rate of movement
#2 - Type of material
#3 - Nature of movement
Types Of Mass Wasting:

## Slide 3: Some Common Types Of Mass Wasting:
Creep
Flow
Torrent
Avalanche
Slump
Slide
Fall
Three distinct physical events occur during a landslide:
the initial slope failure,
the subsequent transport,
and the final deposition of the slide materials.

## Slide 4
Factors which
Contribute to
Mass Wasting:

## Slide 5: Many factors contribute to the instability of slopes, but the general controlling factors are:
The nature of the soil or material in question
The nature of the underlying bedrock
The configuration of the slope, vegetation etc.
The geometry of the slope, angle etc.
Groundwater or local fluid conditions

## Slide 6
Undercutting of a slope by stream erosion, wave action, glaciers, or human activity such as road building,
Intense or prolonged rainfall, rapid snowmelt, or sharp fluctuations in ground-water levels,
Shocks or vibrations caused by earthquakes or construction activity,
Loading on upper slopes, or
A combination of these and other factors.

## Slide 7
How Can We
Control
Mass Wasting:

## Slide 8
METHOD OF CONTROL:
Protective Structures
Slope Modification
            Reduce Slope Angle
            Support Material @ Slope Base
            Reduce weight on slope
Fluid Removal
Slope Stabilization
        Retaining Walls
        Coating Exposed Slopes
        Steel bolts/Anchors
        Vegetation

## Slide 9
Protective Structures:

## Slide 10
Harvey Creek Dam -
Preventing Debris Flow @ Lion's Bay!

## Slide 11
Same Thing - Different Angle!

## Slide 12
Slope Modification:
    Reduce Slope Angle
    Support Material at Slope Base
    Reduce weight on slope

## Slide 13
Reduce Slope Angle – the further below 38 degrees
(angle of repose)…the less likely a slide is!
25 Deg.

## Slide 14
Support Material at Slope Base:

## Slide 15
Reduce weight on slope

## Slide 16
This Would Be
A Bad Idea:

## Slide 17
Fluid Removal:

## Slide 20
Slope Stabilization:
        Retaining Walls
        Coating Exposed Slopes
        Steel bolts/Anchors
        Vegetation

## Slide 21
Retaining Walls

## Slide 23
        Coating or Covering Exposed Slopes

## Slide 24
a spray on concrete type material!

## Slide 25
lining the creek beds with concrete or boulders
is common...

## Slide 26
Nets are also a common "coating"

## Slide 28
Steel bolts/Anchors

## Slide 29
Vegetation

## Slide 30
How Do Landslides
Effect Us?

## Slide 31
The negative economic effects of landslides include:
The cost to repair structures - roads, dams, bridges, buildings, etc.
loss of property value,
disruption of transportation routes,
medical costs in the event of injury,
indirect costs such as - lost timber, fish stocks, and other resources,
Water availability, quantity and quality can be affected by landslides.
Geotechnical studies and engineering projects to assess and stabilize potentially dangerous sites can be costly.

## Slide 32
Some Historical
Mass Wasting Events
In B.C.

## Slide 33
Before debris flow of 1921
Brittania Beach:

## Slide 34
After flow!!

## Slide 35
Hope Slide Now

## Slide 36
Logger's Creek, B.C. 1991 :
Failure is described as a medium-scale rockslide along the Squamish Highway, BC.
Cost $7 million for repairs and preventative structures
The slide closed both the highway and the B.C. Rail track for two weeks while clean up crews removed the debris.

## Slide 37
Sea to Sky rock fall
- Highway 99, B.C. 2008